## Slide 1: FCCS Fire POTENTIALS
Sam Sandberg
Susan Prichard
Cynthia Riccardi
Mark Schaaf
Roger Ottmar
Technical Fire Management
February 2012

## Slide 2
Potential codes:
Reaction Potential
Spread Potential
Flame length Potential
Crown Fire Initiation Potential
Crown-crown Transmissivity Potential
Crown Fire Rate of Spread Potential
Flame Available
Fuel
Smoldering Available
Fuel
Residual Available Fuel
Surface Fire Behavior Potential
Crown Fire Potential
Available Fuel Potential
4 6 3
FCCS Fire Potentials
4 = moderate surface fire
6 = average crowning potential
3= below average available fuel
(indices on a scale of 0 to 9)
Notes: Warning: point release will change crown fire potentials to Schaaf et al specifications.

## Slide 3
Surface fire behavior - predictions of relative and actual surface fire behavior (reaction intensity, rate of spread, and flame length) based on benchmark environmental conditions.
Crown fire potentials – index only of crown fire initiation, transmissivity and rate of spread.
Available fuel potentials – tons/acre of available fuel under dry conditions.
Overview

## Slide 4
Environmental Scenarios
Default
4 mph windspeed
No slope
Dry fuel moisture scenario
- 6.5% dead FM
- 60% nonwoody FM
- 90% shrub FM
Surface fire behavior
Fuel moisture scenario (%)
Midflame windspeed (mph)
Slope gradient (%)

## Slide 5
Part I. FCCS Surface Fire Behavior
Reaction intensity
(BTU/ft2-min)
Rate of spread (ft/min)
Flame length (ft)

## Slide 6
Surface Fire Behavior Report

## Slide 7: Comparison of FCCS and Rothermel’s Spread Model
 | ROTHERMEL (1972) | FCCS (2007)
ASSUMPTIONS | Steady state head fire Flaming front (fine fuels) Uniform fuel, FM, wind, slope Homogenous surface fuels | Same Same Same Heterogeneous surface fuels (4 layers)
OBJECTIVE | Support fire management operations in standard fuels under changing weather conditions. | Compare fire behavior between varying fuelbed characteristics and changing weather conditions
APPLICATIONS | Surface fire behavior modeling | Surface fire behavior modeling Fire effects modeling Fuel treatment assessment Habitat assessments
FUEL CHARACTERISTICS | Stylized fuel models | Realistic (measured) fuel characteristics
CROSSWALK | Fuel models cannot be crosswalked to realistic fuels | Crosswalk from fuelbeds to fuel models (original 13 and standard 40)

## Slide 8
.
Small Woody
Litter
Grass
Shrubs

## Slide 9
Fuel loading
Reaction velocity
Moisture damping)
Heat content
Mineral damping
FCCS
Reaction Intensity (IR) =  [ ’max ’ wn h sm]
Reactive load
Efficiency
Reaction Intensity Equation
Shrubs
Nonwoody
Woody
LLM
Rothermel (1972)
Reaction Intensity (IR) =  ’ wn h sm

## Slide 10
Chart: 
| 1 Black cottonwood -Douglas-fir - quaking aspen riparian | 14 California black oak woodland | 36 California live oak -- blue oak woodland | 43 Arizona white oak -gray oak -Emory oak woodland | 71 Ohia / Florida hopbush - kupaoa forest | 72 Ohia / uluhe forest | 73 Koa / pukiawe forest | 77 Eucalyptus plantation forest | 90 White oak - northern red oak forest | 93 Paper birch -- quaking aspen forest | 94 Balsam poplar - quaking aspen forest | 110 American beech -- yellow birch -- sugar maple forest | 123 White oak - northern red oak - black oak - hickory forest | 129 Green ash - American elm forest | 142 Quaking aspen - paper birch forest | 180 Red maple - oak - hickory - sweetgum forest | 186 Turkey oak - bluejack oak forest | 224 Quaking aspen forest | 225 Quaking aspen forest (Rx burn) | 260 Ohia / uluhe forest | 264 Post oak - blackjack oak forest | 266 Sugar maple - basswood forest | 269 Sugar maple - yellow poplar - American beech - oak forest | 272 Mangrove forest | 274 American beech - sugar maple forest | 275 Chestnut oak - white oak - northern red oak forest | 283 Willow oak - laurel oak - water oak forest | 284 Green ash - American elm - silver maple - cottonwood forest
RI_LLM (BTU/ft2/min) | 549.8654 | 935.345 | 572.8049 | 308.6643 | 394.1238 | 407.9324 | 380.3882 | 407.9324 | 407.9324 | 449.7738 | 418.4331 | 428.5544 | 1414.2759 | 407.9324 | 451.9568 | 407.9324 | 417.5226 | 398.3954 | 403.6823 | 407.9324 | 394.1238 | 407.9324 | 407.9324 | 244.7798 | 407.9324 | 402.4 | 407.9324 | 407.9324
RI_Woody (BTU/ft2/min) | 16.1246 | 382.8493 | 450.0098 | 204.2992 | 494.8355 | 71.9155 | 1064.5955 | 1952.447 | 52.9614 | 283.4923 | 146.9336 | 390.8903 | 777.2063 | 130.887 | 1022.3724 | 649.6814 | 250.8109 | 193.4042 | 119.1122 | 124.6033 | 297.4401 | 741.1527 | 1008.9843 | 443.3158 | 522.539 | 916.6512 | 146.6265 | 49.7854
RI_Nonwoody (BTU/ft2/min) | 345.3794 | 603.0731 | 2015.0447 | 2126.0952 | 2895.7249 | 16765.027 | 8932.09 | 167.7745 | 17.2081 | 73.7915 | 102.2851 | 354.9791 | 250.4621 | 378.839 | 423.5568 | 1173.7998 | 526.5308 | 3948.3523 | 2206.477 | 22861.648 | 5368.9834 | 1609.2711 | 2039.277 | 55.2691 | 3280.9468 | 611.8754 | 37.2404 | 297.3471
RI_Shrub (BTU/ft2/min) | 226.9332 | 60.6618 | 1650.287 | 208.8772 | 4269.623 | 145.7109 | 672.8697 | 1434.319 | 79.9354 | 95.2425 | 64.6665 | 16.7631 | 254.3767 | 81.385 | 255.3124 | 312.6582 | 430.5634 | 166.4791 | 243.0911 | 18.7387 | 348.1878 | 181.0596 | 119.5175 | 1187.5634 | 317.3395 | 2553.9714 | 216.4357 | 54.5143
Reaction Intensity (hardwood forests)
Shrubs
Nonwoody
Woody
Litter

## Slide 11
Reaction Intensity (conifer forests)
Chart: 
| 2 Western hemlock - western redcedar - Douglas-fir forest | 4 Douglas-fir / ceanothus forest | 5 Douglas-fir - white fir forest | 8 Western hemlock - Douglas-fir - western redcedar / vine maple forest | 9 Douglas-fir - western hemlock - western redcedar / vine maple forest | 10 Western hemlock - Douglas-fir - Sitka spruce forest | 11 Douglas-fir / western hemlock - Sitka spruce forest | 12 Red fir - mountain hemlock - lodgepole pine - western white pine forest | 13 Mountain hemlock - Pacific silver fir forest | 15 Jeffrey pine - red fir - white fir / greenleaf - snowbrush forest | 17 Red fir forest | 18 Douglas-fir / oceanspray forest | 19 White fir - giant sequoia - sugar pine forest | 20 Western juniper / curl-leaf mountain mahogany woodland | 21 Lodgepole pine forest (young) | 22 Lodgepole pine forest (mature) | 23 Lodgepole pine forest (beetle attack) | 24 Pacific ponderosa pine - Douglas-fir forest | 25 Pinyon - Utah juniper forest | 26 Interior ponderosa pine - limber pine forest | 27 Ponderosa pine - two needle pinyon - Utah juniper forest | 29 Interior ponderosa pine - Engelmann spruce - Douglas-fir forest | 32 Ponderosa pine / pinyon pine - Utah juniper forest | 34 Interior Douglas-fir - interior ponderosa pine / gambel oak forest | 37 Ponderosa pine - Jeffrey pine forest | 47 Redwood - tanoak forest | 52 Douglas-fir - Pacific ponderosa pine / oceanspray forest | 53 Pacific ponderosa pine forest | 54 Douglas-fir - white fir - interior ponderosa pine forest | 59 Subalpine fir - Engelmann spruce - Douglas-fir - lodgepole pine forest | 61 Whitebark pine / subalpine fir forest | 67 Interior ponderosa pine - Douglas-fir forest | 70 Subalpine fir - lodgepole pine - whitebark pine - Engelmann spruce forest | 75 Slash pine / New Caledonia pine forest | 76 Slash pine / molasses grass forest | 85 Black spruce / lichen forest
RI_LLM (BTU/ft2/min) | 653.2378 | 575.3684 | 541.6158 | 630.8942 | 646.2224 | 645.8466 | 644.8154 | 660.3389 | 327.9479 | 912.4594 | 628.373 | 526.7226 | 622.8518 | 621.7565 | 616.9871 | 600.5665 | 586.6858 | 984.7567 | 581.5494 | 1729.5029 | 866.7359 | 387.6278 | 1530.6377 | 708.0872 | 644.5122 | 630.8821 | 835.7847 | 1383.9442 | 745.4587 | 684.8799 | 492.7288 | 588.3873 | 557.0212 | 1874.2501 | 922.9739 | 901.9288
RI_Woody (BTU/ft2/min) | 1420.3462 | 556.4377 | 956.5505 | 1442.497 | 2236.1755 | 1345.5386 | 1622.9146 | 531.7369 | 465.8273 | 252.1668 | 1781.3726 | 389.018 | 1092.6125 | 31.7923 | 0.008147 | 34.0697 | 351.137 | 137.8703 | 425.3043 | 67.956 | 214.9015 | 1476.3953 | 440.6193 | 799.1269 | 488.0835 | 1129.9375 | 480.9832 | 504.6057 | 140.5876 | 905.8031 | 301.8997 | 896.5851 | 756.3616 | 491.0356 | 102.2409 | 363.4961
RI_Nonwoody (BTU/ft2/min) | 636.3113 | 2680.7732 | 732.2372 | 68.1045 | 564.5763 | 1554.7983 | 1101.733 | 266.1803 | 756.9035 | 254.7371 | 304.8585 | 834.1221 | 28.5498 | 1300.3375 | 7.3174 | 459.3918 | 748.2998 | 2284.0266 | 267.1556 | 368.6945 | 1812.8093 | 951.0129 | 0 | 1333.2937 | 1781.9167 | 2198.8645 | 1014.06 | 351.8045 | 262.7604 | 1222.6294 | 1062.8711 | 3868.141 | 923.5742 | 0 | 7720.913 | 267.5409
RI_Shrub (BTU/ft2/min) | 4668.5737 | 3737.7136 | 6827.0957 | 797.2852 | 2458.0405 | 925.0905 | 807.3616 | 6.4006 | 511.7653 | 2695.4463 | 0 | 139.7583 | 79.3058 | 693.0606 | 0.0089619 | 0.18303 | 921.1039 | 0 | 554.5554 | 2291.0444 | 3730.5637 | 2749.767 | 34.1939 | 274.3702 | 8037.081 | 4852.8467 | 222.8685 | 0 | 13.232 | 305.549 | 856.3079 | 254.2898 | 446.1307 | 71.4739 | 1.3288 | 1127.3553
Shrubs
Nonwoody
Woody
Litter

## Slide 13
Function of:
  Reaction intensity
  Propagating energy flux
  Heat sink of unburned fuels in advance of flaming front
FCCS Surface Fire Behavior Rate of Spread Equation
Rate of Spread = Heat Source
Heat Sink
Notes: Important point: We consider each fuelbed component acts separately as a heat sink. Rate of spread is proportional to heat source vs. heat sink. No longer requires an artificial fuelbed depth and scaling necessary in a fuel model out of the process. Validated by 216 fuelbeds. This really fixed a couple of deficiencies in Rothermel formulation – these used to be overcome by adjusting fuel models.

## Slide 14
(Heat sink weighted by cover and reactive load by fuel stratum)
Rate of Spread Equation
(Heat source)
Qig = heat of preignition (heat required for pyrolysis)
= effective heating number (preheated portion)
= bulk density of fuelbed element
= depth of fuelbed element
 = prop ground surface covered by fuelbed element
Rothermel ROS =
ROS =
(Heat sink)

## Slide 15
Grassland fuelbeds vs. standard fuel models
Chart: 
| GR1 | GR2 | GR3 | GR4 | GR5 | GR6 | GR7 | GR8 | GR9 | 261 Pili grass - broomsedge bluestem grassland | Willow / sedge grassland | 79 Pili grass - broomsedge bluestem grassland | 57 Wheatgrass - cheatgrass grassland | 83 Molasses grass grassland | 236 Tobosa - grama grassland | 81 Pukiawe / Columbia bluestem grassland | 80 Fountain grass grassland | 40 Tobosa - grama grassland | 63 Showy sedge - alpine black sedge grassland | 213 Wheatgrass - cheatgrass grassland | 66 Bluebunch wheatgrass - bluegrass grassland | 41 Idaho fescue - bluebunch wheatgrass grassland | 97 Cottongrass grassland | 235 Idaho fescue - bluebunch wheatgrass grassland | 262 Molasses grass grassland | 99 Bluejoint reedgrass grassland | 280 Bluestem - Gulf cordgrass grassland | 221 Wheatgrass - ryegrass grassland | 65 Purple tussockgrass - California oatgrass grassland | 131 Bluestem - Indian grass - switchgrass grassland | 203 Sawgrass - Muhlenbergia grassland | 175 Smooth cordgrass - black needlerush grassland | 176 Smooth cordgrass - black needlerush grassland | 100 Altai fescue grassland
ROS (ft/min) | 12 | 25.5 | 36.7 | 51.8 | 43.2 | 52.3 | 77.3 | 80.3 | 126.9 | 1.9456 | 2.6532 | 2.687 | 3.2136 | 3.4034 | 6.8513 | 9.0327 | 13.7639 | 14.2835 | 14.5569 | 22.6129 | 23.6535 | 29.0412 | 36.153 | 41.2972 | 42.1481 | 54.65 | 59.397 | 62.8379 | 62.9803 | 67.4401 | 99.2513 | 104.388 | 106.1368 | 110.7946
FL (ft) | 1.7 | 4 | 6.1 | 7.5 | 9.5 | 11.4 | 16 | 20.5 | 27.9 | 2.4635 | 1.1452 | 3.186 | 0.7383 | 5.2851 | 0.82909 | 6.297 | 9.2766 | 2.4856 | 4.8691 | 2.4331 | 4.5436 | 4.6261 | 11.9006 | 9.8068 | 16.3221 | 14.6853 | 13.1524 | 3.4796 | 9.6801 | 12.7445 | 15.7647 | 17.5112 | 15.9748 | 19.6392

## Slide 16
Shrub fuelbeds: rate of spread
Chart: 
| SH1 | SH2 | SH3 | SH4 | SH5 | SH6 | SH7 | SH8 | SH9 | Creosote bush shrubland | Western juniper / sagebrush -- bitterbrush shrubland | Gambel oak / big sagebrush shrubland | Turbinella oak -- alderleaf mountain mahogany shrubland | Pitch pine / scrub oaks shrubland | Willow -- mountain alder shrubland | Gambel oak / big sagebrush shrubland | Huckleberry - heather shrublands | Rhododendron -- blueberry -- mountain laurel shrubland | Sagebrush shrubland | White leadtree / Guinea grass shrubland | Marsh Labrador tea -- lingonberry tundra shrubland | Chamise chaparral shrubland | Sagebrush shrubland | Florida hopbush - Mauna Loa beggarticks shrubland | Huckleberry -- heather shrubland | Sagebrush shrubland | Pond pine / gallberry -- fetterbush shrubland | Saw palmetto / three-awned grass shrubland | Scrub oak chaparral shrubland | Gallberry -- fetterbush shrubland | Sagebrush shrubland | Coastal sage shrubland
ROS (ft/min) | 1.7 | 2.3 | 3.1 | 20.8 | 44.4 | 18.6 | 29.2 | 17.5 | 32.2 | 0.24928 | 0.76239 | 2.4712 | 2.8941 | 3.4052 | 3.6169 | 4.9163 | 4.9615 | 5.6514 | 5.9737 | 6.8023 | 6.9901 | 8.7455 | 9.0361 | 10.1485 | 12.591 | 18.1444 | 18.6161 | 19.8925 | 20.7116 | 20.9861 | 25.221 | 37.501
FL (ft) | 0.7 | 1.9 | 2.1 | 5.8 | 12.1 | 8.2 | 11.5 | 9.2 | 15.2 | 0.51101 | 1.395 | 1.8575 | 2.1625 | 1.4016 | 1.8956 | 2.6974 | 1.7552 | 2.8465 | 1.5995 | 5.7682 | 3.3258 | 6.6238 | 2.5851 | 6.7716 | 5.0416 | 4.8466 | 7.4322 | 7.3694 | 6.866 | 8.2082 | 7.7322 | 10.2487

## Slide 17
Flame Length Equation
FL = 0.045 x (RI x ROS x Flame Residence Time)0.46
RI = Reaction intensity
ROS = Rate of spread

## Slide 18: Part II. Crown Fire Potentials
  Probability for surface fire to initiate into tree crowns
  Index of the ability of crowns to carry crown fire
  Index of the crown fire rate of spread
Crown Fire
Initiation
Potential
Crown-Crown
Transmissivity
Potential
Crown Fire
Rate of spread
Potential

## Slide 19: Crown Fire Initiation Potential
CI =
Surface fireline intensity
Critical fireline intensity
Where:
Surface fireline intensity (Btu/ft2/min) =
ƒ (surface reaction intensity, flame residence
time, and rate of spread)
Critical fireline intensity (Btu/ft2/min) =
ƒ ( constants, canopy base height,
canopy FM)

## Slide 20: Crown-crown Transmissivity Potential
TC =
ƒ (canopy cover, leaf area index, windspeed)

## Slide 21: Crown Fire Rate of Spread Potential
RC =
Canopy heat source
Canopy heat sink
Where:
Heat source =
ƒ (RI surface, RI canopy, propogating flux ratio, windspeed factor)
Heat sink =
ƒ (heat sink of canopy wood (i.e., branches), canopy foliage, and surface fuels )

## Slide 22: Part III. Available Fuel Potential
Litter
“Flash” Fuels
1-hr
Log
100-hr
Pyrolysis zone
Flame available
Smolder available
Residual available
Flame Available Fuel
Potential
Smoldering Available Fuel
Potential
Residual Available Fuel
Potential

## Slide 23
FCCS Applications Translating fuelbeds into fire hazard mapping and assessment

## Slide 24
http://www.fs.fed.us/pnw/fera/fccs/pubs.shtml
For More Information