## Slide 1: Get Moving With Core Motion!
http://www.slideshare.net/jblocksom/core-motion-presentation
Jonathan Blocksom
Tuesday Sept 28 2010 2:00 – 3:15 PM

## Slide 2: Agenda
Intro
SDK
Experiments
Q & A
Intro level, but lots of code

## Slide 3: About Me
Jonathan Blocksom
blocksom@gollygee.com
augmentedjonathan.tumblr.com
@jblocksom
Computer Vision Software Engineer, SET Corp
Computer Graphics background
Several years working with Remote Sensing

## Slide 4: Meet Core Motion!
Core Motion Framework: High level interface to the orientation and movement data from the device
Based on Accelerometer and Gyroscopes
Acceleration, Gravity, Rotational Acceleration
High level filtering

## Slide 5: Core Motion isn’t…
For GPS data
  That’s Core Location (LocationManager)
For Compass data
  Also Core Location
High Level Motion Events
  Orientation change
  Shake events
Perfect

## Slide 6: Quick Demo
CoreMotionTeapot (WWDC 2010 sample code)

## Slide 7: Accelerometer
Available since iPhone 1
Consider it a “Gravity Detector”
Noisy
iPad, iPhone 4: STMicro STM33DH 3-axis accelerometer
Photo by David Hodson http://www.ifixit.com/Guide/Image/meta/IP1qEpYFQSSqwSbg

## Slide 8: Gyroscopes
New in iPhone 4, iPod Touch 4
Detects rotation rate along three axis
Chip datasheet: http://www.st.com/stonline/products/literature/ds/17116.pdf
200/500/2500 dps (degrees per second)
0.03 dps error

## Slide 9: Gyro Teardown
http://www.ifixit.com/Teardown/iPhone-4-Gyroscope-Teardown/3156/1
Andrew Bookholt:
http://www.ifixit.com/Guide/Image/meta/UurGsklhtJRW2uuB (left)
http://www.ifixit.com/Guide/Image/meta/MeunHawo54qPRY5S (right 1)
Miroslav Djuric
http://www.ifixit.com/Guide/Image/meta/RUQLo2PP1oqVtVsD (right 2)

## Slide 10: Accelerometer, Gyro & Device Motion
Accelerometer
Gyro
Device Motion
x, y, z
yaw, pitch, roll
Gravity
User acceleration
Attitude
Rotation Rate

## Slide 11: Supported Devices
 | iPhone 1 | iPhone 3G | iPhone 3GS | iPhone 4 | iPod Touch | iPod Touch 4 | iPad
Accelerometer | Y | Y | Y | Y | Y | Y | Y
Gyros |  |  |  | Y |  |  | 
iOS 4 |  | Y | Y | Y |  | Y | 
If we must…
Yay!
No.
iPhone 4 iPod Touch 4
iPhone 3GS
iPod Touch
iPad w/ iOS 4
iPhone 1
iPad iOS 3.x

## Slide 12: Classes
Class | Description | 
CMMotionManager | The Gateway | 
CMAccelerometerData | Acceleration data X, Y, and Z relative to device In G’s | 
CMAttitude | Orientation Roll, Pitch, Yaw Rotation Matrix Quaternion | 
CMDeviceMotion | Roll up of sensors Differentiates gravity from user acceleration | 
CMGyroData | Rotational Velocity | 
CMLogItem | Timestamped Measurement | Parent Class for measurements

## Slide 13: CMMotionManager
Tells you what’s available
  is<Acclerometer|DeviceMotion|Gyro>Available
Sets the update intervals
  set<…>UpdateInterval
Starts and stops updates
  start<…>Updates
  start<…>UpdatesToQueue:withHandler:
  stop<…>Updates
Lets you poll for updates
  accelerometerData
  gyroData
  deviceMotion

## Slide 14: CMMotionManager
CMMotionManager *mgr = [[CMMotionManager alloc] init];
Initializes reference frame at construction
Only make one of these for your app

## Slide 15: Core Motion Coordinate System Quick Reference
yaw
pitch
roll
x
z
y
Accelerometer
Gyroscopes

## Slide 16: CMAccelerometerData
acceleration CMAcceleration struct: typedef struct { double x; double y; double z; } CMAcceleration;
Measured in G’s

## Slide 17: CMGyroData
YAGNI
Gyro’s have bias; DeviceMotion fusion algorithms remove this
Get orientation from DeviceMotion instead

## Slide 18: CMDeviceMotion
CMAttitude attitude
CMRotationRate rotationRate
CMAcceleration gravity
CMAcceleration userAcceleration

## Slide 19: DEMO
MacCMViewer
CMIPViewer
Source code available: http://bitbucket.org/jblocksom/coremotionviewer

## Slide 20: MacCMView: What’s Going On?
Mac opens socket; iPhone connects
iPhone sends CM updates to Mac
Mac uses rotation matrix for display
From CMAttitude

## Slide 21: CMAttitude
Rotation as
  Yaw, Pitch, Roll
  Quaternion
  Rotation Matrix
multiplyByInverseOfAttitude:

## Slide 22: Why Quaternions?
Great technique for representing rotations
Mutiplying q1 and q2 is composing rotations
Can easily pull out axis / angle
Avoids “Gimbal Lock”
http://en.wikipedia.org/wiki/Quaternions_and_spatial_rotation is a pretty good treatment
Graphics Gems textbooks
Notes: Wikipedia rant – great for Epipolar Geometry, terrible for Quaternions

## Slide 23: multiplyByInverseOfAttitude:
Teapot Demo revisited

## Slide 24: Core Motion in Simulator
Accelerometer: Not available
Gyros: Not available
Device Motion: Not available
Workaround thoughts…

## Slide 25: Final Steps: App Requirements
Add UIRequiredDeviceCapabilities for accelerometer gyro
Not needed for orientation / shake events
See Event Handling Guide, “Setting Required Hardware Capabilities for Accelerometer and Gyroscope Events”

## Slide 26: Experiments
iPhone 3GS vs iPhone 4
Intertial Navigator
Salad Spinner

## Slide 27: Further Reading
Event Handling Guide for iPhone OS
  Look under “Motion Events”
  Section titled “Core Motion”
Core Motion framework reference
Sample Code
  WWDC ’10: CoreMotionTeapot
iPhone Sensor Group?